## Slide 1
Exercise 8: Changing input data
Peter Burek, Mikhail Smilovic, Luca Guillaumot
International Institute for Applied Systems Analysis
Research Scholars at
Water Program

## Slide 2: Changing input data
0. What you need
What is netCDF
Display netCDF files
Change ksat2 (saturated soil conductivity layer 2) in ArcGIS
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 3: Changing input data
0. What you need
A Geoinformation System e.g. QGIS, ArcGIS
A way to display netCDF files easily e.g.: PANOPLY on Windows https://www.giss.nasa.gov/tools/panoply/ ncview on Linux:
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 4: Changing input data
What is netCDF
NetCDF (Network Common Data Form) is a data format like .tif, .jpg
NetCDF is a set of librariesand self-describing, machine-independent data formats that support the creation, access, and sharing of array-oriented scientific data
Mainly used by the meteorological community
Advantage:
netCDF is self-describing, portable, flexible
netCDF is public domain, well documented and used by a growing number of organizations
High efficiency in reading and processing netCDF files (it is fast)
A netCDF file can contain timeseries of spatial data in a compressed way
Disadvantage:
Not so easy to handle
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 5: Changing input data
Examples of netCDF
Digital elevation (source:SRTM) ../CWATM_data/cwatm_input5min/landsurface/topo/dem.nc
Metainformation e.g. - dimension (here without time) - unit
- description
Variables - latitude
- longitude
- elevation
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 6: Changing input data
Examples of netCDF
Monthly industry water demand (calculation Wada et al. 2014) ../CWATM_data/cwatm_input5min/landsurface/waterDemand/industryWaterDemand.nc
Metainformation e.g. - dimension (here with time) - unit
- description
Variables
- latitude
- longitude
- time
- 2 variables
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 7: Changing input data
Take a look at dataset
  Take a look at: https://cwatm.iiasa.ac.at/data.html
  Take a look at ../CWATM_data/cwatm_input30min
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 8: Changing input data
Changing values with CDO (Linux)
CDO (Climate Data Operators)
https://code.mpimet.mpg.de/projects/cdo/
CDO is a collection of command line Operators to manipulate and analyse netCDF data.
There are more than 600 operators available
Metainformation e.g. - dimension (here with time) - unit
- description
cdo expr, ‘ksat2 = ksat2_o * 2’ ksat2.nc ksat22.nc
Multiplying values by two
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 9: Changing input data
Changing values with ArcGis
Open Arcgis
Drop ksat2.nc into “Table of content”
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 10: Changing input data
Changing values with ArcGis
Open toolbox – Spatial Analyst Tool – Map Algebra – Raster calc.
Put in: “ksat2_o” *2
Put in output raster – into the folder of CWATM_exercise8
You have to choose a different name than ksat2_2.tif if there is already a ksat2_2.tif in this folder
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 11: Changing input data
Convert file from .tif to netcdf
Run tif2nc.bat
This will run python tif2netcdf.py
Output is ksat2_2.nc
tif2netcdf.py
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 12: Changing input data
Convert file from .tif to netcdf
Run tif2nc.bat
This will run python tif2netcdf.py
Output is ksat2_2.nc
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 13: Changing input data
Run CWatM twice to see the difference
Run 01_python_example.bat
or python ../CWATM_model/CWatM/run_cwatm.py settings_rhine30min1.ini -l
Output in output1
Run 02_python_example.bat
or python ../CWATM_model/CWatM/run_cwatm.py settings_rhine30min2.ini -l
Output in output2
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 14: Changing input data
Run CWatM twice to see the difference
Run 01_python_example.bat
or python ../CWATM_model/CWatM/run_cwatm.py settings_rhine30min1.ini -l
Output in output1
Run 02_python_example.bat
or python ../CWATM_model/CWatM/run_cwatm.py settings_rhine30min2.ini -l
Output in output2
Difference settings_rhine30min2.ini vs. settings_rhine30min2.ini
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.

## Slide 15: Changing input data
Have a look at rhine8.xlsx to see the difference
Notes: Improvement in resolution of CWatM model for basin analysis to show more details locally.